## Slide 1: Visual-Weld v7.5

## Slide 2: Outline
What is Visual-Weld?
Model Building
Welding Advisor
Weld Utilities
Heat Treatment Advisor
Post Processing & Report Generation
Tools & Customization
Discussions

## Slide 3: What is Visual-Weld?
Visual-Weld is the new-generation easy to use welding & Heat Treatment simulation tool developed in Visual-Environment which encompasses the complete workflow for a realistic simulation based design. It offers the full set of welding engineering methodologies needed by designers, process planners and manufacturing practitioners. Visual-Weld coupled with Visual-Mesh and Visual-Viewer covers all the activities of a Welding Engineer starting from interfacing to CAD formats, CAD cleanup, meshing, model set-up, post processing using one single data model.

## Slide 4: Work flow
Visual-Mesh
Visual-Weld
SYSWELD
Visual-Viewer (Weld)
CAD
MESH
MESH
WELD Definition
Solve
Results
CAD DATA
T-JOINT.iges
MESH DATA
T-JOINT.vdb
MESH & WELD DATA
T-JOINT.vdb
Results
T-JOINT.fbd
or *.dsy,*.erf

## Slide 5: File types
*.vdb - Visual Mesh file with all mesh data
*.ASC – Sysweld File with all FEM data
*.Dat files
Meshing
*.prj – Project file generated with a Sysweld Advisor or an Excel tool
Project definition
*.fdb – Out of a file type TIT converted hoops result file (Stresses, Strains
Converted Result Files
*.TIT – Sysweld result files in a binary format (DISP (nodes), FORCES (GP), etc.
Result Files
*.DAT – Files with solver commands generated out of a project file
Solver Command File
File Types Welding
1
2
3
4
5

## Slide 6: Graphical User Interface
Access various functions to thematic menu system
Easy accessible tool bars
Explorer Window, where you can visualize and manipulate the model objects tree
Model Window area, where models are displayed in one or several windows.
Console Window, where system messages are displayed.
Context Bar , where in user can switch to different context to Build, Define or Visualize results

## Slide 7
The Entity Selector toolbar allows you to select and modify several entities at one time, using different methods.
ID input
List Selection
Graphical pick
Advanced selection
Many more…
Entity Selector

## Slide 8
Display Control
  Fast display control
    Show selected, all, unselected
    Hide selected, all, unselected
    Reverse visibility
    Show / Mask part or element contain in a circle of 10 mm radius (in the example)
  View and Display mode tool bars

## Slide 9
View Manipulator (Compass)
View Manipulator (Compass)
  Interactive view manipulator to reduce mouse movement and better model handling.
    2D Rotation
    Horizontal/Vertical Translation
    Horizontal/Vertical Rotation
    Axis Translation
    Axis Rotation
    View Orientation
    Mirror View and
    Zoom
  Options to Control the view manipulations

## Slide 10: Outline
What is Visual-Weld?
Model Building
Welding Advisor
Weld Utilities
Heat Treatment Advisor
Post Processing & Report Generation
Tools & Customization
Discussions

## Slide 11
Model Building
Start with Visual–Mesh preprocessor, in order to create geometry, mesh and groups, from scratch or starting from geometry data exported from external CAD systems
Visual-Mesh
CAD
MESH
CAD DATA
T-JOINT.iges
MESH DATA
T-JOINT.vdb

## Slide 12
Model Building
Collector Manager
Collector Manager is an versatile utility that allows users to manage collectors. It allows you to create, edit, delete and visualize collectors which are very important in any welding simulation

## Slide 13
Some of key features are listed below.
  Options to list collectors page wise and choose lines per page for easy listing.
  Filtering option based on Ids.
  Option to display model in boundary mode for easy visualization of collectors.
  Option to list all or only visible collectors.
  Options to add, remove and move entities from collectors.
  Provision to sort columns by clicking on column header.
  Editable name field.
  ‘Save’ option to save all the information in .csv format
Model Building
Collector Manager

## Slide 14: Outline
What is Visual-Weld?
Model Building
Welding Advisor
Weld Utilities
Heat Treatment Advisor
Post Processing & Report Generation
Tools & Customization
Discussions

## Slide 15: Welding Advisor
  An easy-to-use guided work-flow based interface requiring minimum input; Define and solve weld problems; Set-up Single-Pass and Multi-Pass Welding simulations
Welding Advisor
Project Description
Global Parameters
Material Properties
Heat Treatment Process
Cooling Condition
Clamping Conditions
Loads & Deformations
Solution Parameters

## Slide 16: Welding Advisor Project Description
  Define project name and working directory with other basic information for project identification;
  Project name will be used for all created files and they will be stored in the working directory
Welding Advisor
Project Description
Global Parameters
Component Properties
Welding Process
Cooling Condition
Clamping Conditions
Loads & Deformations
Solution Parameters

## Slide 17: Welding Advisor Global Parameters
    Set the computation option to be used for the project;
    Default computation option is selected automatically based on the loaded mesh;
Welding Advisor
Project Description
Global Parameters
Component Properties
Welding Process
Cooling Condition
Clamping Conditions
Loads & Deformations
Solution Parameters

## Slide 18: Welding Advisor Component Properties
    Assign materials to all components and/or filler material defining the weld problem. You can select Parts and/or Collectors for components process type.
Welding Advisor
Project Description
Process Definition
Component Properties
Welding Process
Cooling Condition
Clamping Conditions
Loads & Deformations
Solution Parameters

## Slide 19: Welding Advisor Welding Process
    Define all required trajectories;
    Choose different process types either pre defined or user defined;
    Define all properties for heat source with diving.
Welding Advisor
Project Description
Process Definition
Material Properties
Welding Process
Cooling Condition
Clamping Conditions
Loads & Deformations
Solution Parameters

## Slide 20: Welding Advisor Welding Process - Automatic Weld Trajectory
    Create Weld trajectories automatically;
    Directly edit entities or visualize them in explorer
Welding Advisor
Project Description
Process Definition
Material Properties
Welding Process
Cooling Condition
Clamping Condition
Loads & Deformations
Solution Parameters
WELD LINE

## Slide 21: Welding Advisor Cooling Condition
    Define heat exchange condition;
    Choose from Free cooling and/or Forced cooling
Welding Advisor
Project Description
Process Definition
Component Properties
Welding Process
Cooling Condition
Clamping Condition
Loads & Deformations
Solution Parameters

## Slide 22: Welding Advisor Clamping Condition
    Define all Clamps required for complete welding -
      Elastic, Rigid, Symmetry, Unclamped;
    Define clamping condition using the clamps defined;
    Directly Visualize and edit entities in explorer
Welding Advisor
Project Description
Process Definition
Component Properties
Welding Process
Cooling Condition
Clamping Condition
Loads & Deformations
Solution Parameters

## Slide 23: Welding Advisor Loads & Deformations
Welding Advisor
Project Description
Process Definition
Material Properties
Heat Treatment Process
Cooling Condition
Clamping Condition
Loads & Deformations
Solution Parameters
    Define all loads and/or deformations;
      Displacements, Force, Pressure;
    Define loading conditions using the loads defined.

## Slide 24: Welding Advisor Solution Parameters
    Solve Set various solver parameters;
    Generate the input data;
Welding Advisor
Project Description
Process Definition
Component Properties
Welding Process
Cooling Condition
Clamping Condition
Loads & Deformations
Solution Parameters
MESH & WELD DATA
T-JOINT.vdb

## Slide 25: Outline
What is Visual-Weld?
Model Building
Welding Advisor
Weld Utilities
Heat Treatment Advisor
Post Processing & Report Generation
Tools & Customization
Discussions

## Slide 26: Weld Utilities Skin Generation and Element
Weld Utilities
Basic Utilities
Job Submission
Export to Pam Assembly
Welding Sequence Visualization

## Slide 27: Weld Utilities Welding Sequence Visualization
Weld Utilities
Welding Sequence Visualization
Job Submission
Export to Pam Assembly
Basic Utilities

## Slide 28: Weld Utilities Computation Manager
Weld Utilities
Welding Sequence Visualization
Computation Manager
Export to Pam Assembly
    An easy-to-use utility to manage complex solver runs efficiently;
    Gives you an overview of project contents;
    Allows you to control solver jobs;
  Color coding of cells based on solver run status -
    Gray: No computation;
    Blue: Computation running;
    Orange: Problem during computation;
    Green: Computation done;
Basic Utilities

## Slide 29: Weld Utilities Export to PAM Assembly
Weld Utilities
Welding Sequence Visualization
Computation Manager
Export to PAM Assembly
    Export the results obtained to PAM Assembly;
    Choose from Block or Slice options;
Basic Utilities

## Slide 30: Outline
What is Visual-Weld?
Model Building
Welding Advisor
Weld Utilities
Heat Treatment Advisor
Post Processing & Report Generation
Tools & Customization
Discussions

## Slide 31: Heat Treatment Advisor
The Heat Treatment Advisor includes all you need to set up, simulate, and analyze heat
treatment problems.
Heat Treatment Advisor
Project Description
Process Definition
Material Properties
Heat Treatment Process
Clamping Condition
Loads & Deformations
Solution Parameters
Computation Manager

## Slide 32: Heat Treatment Advisor Project Description
  Enter project details viz. Project Name, Title, Project Path and General description
Heat Treatment Advisor
Project Description
Process Definition
Material Properties
Heat Treatment Process
Clamping Condition
Loads & Deformations
Solution Parameters
Computation Manager

## Slide 33: Heat Treatment Advisor Process Definition
  Select the required processes for heat treatment; Tempering will be supported in the next release;
  Computation Option set automatically. Modify if needed;
  Define cyclic symmetry for 3D models
Heat Treatment Advisor
Project Description
Process Definition
Material Properties
Heat Treatment Process
Clamping Condition
Loads & Deformations
Solution Parameters
Computation Manager

## Slide 34: Heat Treatment Advisor Material Properties
  Assign materials to required groups;
  Filter material automatically based on the selected process type;
Heat Treatment Advisor
Project Description
Process Definition
Material Properties
Heat Treatment Process
Clamping Condition
Loads & Deformations
Solution Parameters
Computation Manager

## Slide 35: Heat Treatment Advisor Heat Treatment Process
  Define Heating, Carburization, quench media and quenching condition;
  You can also define quench media with diving;
Heat Treatment Advisor
Project Description
Process Definition
Material Properties
Heat Treatment Process
Clamping Condition
Loads & Deformations
Solution Parameters
Computation Manager

## Slide 36: Heat Treatment Advisor Clamping Condition
  Define clamps and clamping conditions;
Heat Treatment Advisor
Project Description
Process Definition
Material Properties
Heat Treatment Process
Clamping Condition
Loads & Deformations
Solution Parameters
Computation Manager

## Slide 37: Heat Treatment Advisor Loads & Deformations
  Define loads and loading conditions. This is not mandatory. User can defined loads based on the scenario.
Heat Treatment Advisor
Project Description
Process Definition
Material Properties
Heat Treatment Process
Clamping Condition
Loads & Deformations
Solution Parameters
Computation Manager

## Slide 38: Heat Treatment Advisor Solution Parameters
  Define parameters for computation;
  Use default settings or modify them as needed;
Heat Treatment Advisor
Project Description
Process Definition
Material Properties
Heat Treatment Process
Clamping Condition
Loads & Deformations
Solution Parameters
Computation Manager

## Slide 39: Heat Treatment Advisor Computation Manager
  Solve all Heat Treatment processes in one manager;
  Generate batch scripts for Windows & Linux;
Heat Treatment Advisor
Project Description
Process Definition
Material Properties
Heat Treatment Process
Clamping Condition
Loads & Deformations
Solution Parameters
Computation Manager

## Slide 40: Outline
What is Visual-Weld?
Model Building
Welding Advisor
Weld Utilities
Heat Treatment Advisor
Post Processing & Report Generation
Tools & Customization
Discussions

## Slide 41: Post-Processing Visualization
Post-Processing
Visualization
Report Generation
    Visualize geometry, contours, curves, printing, pattern, vectors display options and report generations

## Slide 42: Post-Processing Visualization
Post-Processing
Visualization
Report Generation
    Visualize geometry, contours, curves, printing, pattern, vectors display options and report generations

## Slide 43: Post-Processing Report Generation
Post-Processing
Visualization
Report Generation
  From Visual Viewer reports can be generated from File -> Preview by giving various input and by using Drawing blocks

## Slide 44: Post-Processing Automatic Report Generation- Welding Simulation
Post-Processing
Visualization
Report Generation
  For Welding scenarios, Auto report generation is provided. On specifying the working project directory, application automatic picking of mesh & result files from the project folder; Fully customizable; Options to export in pdf and pptx formats

## Slide 45: Outline
What is Visual-Weld?
Model Building
Welding Advisor
Weld Utilities
Heat Treatment Advisor
Post Processing & Report Generation
Tools & Customization
Discussions

## Slide 46: Tools & Customization Measure
Tools & Customization
Measure
Customization
General Preferences
  Measure Distance , Angle & Area / Volume;
  Measured quantities dynamically updated during modelling; Option to show/hide measured distances.

## Slide 47: Tools & Customization Customization
Tools & Customization
Measure
Customization
General Preferences
  Customize menus and toolbars.

## Slide 48: Tools & Customization Customization
Tools & Customization
Measure
Customization
General Preferences
  Customize Keyboard shortcuts, mouse buttons, appearance and much more…

## Slide 49: Tools & Customization General Preferences
Tools & Customization
Measure
Customization
General Preferences
  Manage window behaviour;
  Directory setting;
  Selection and View Setting;
  Console settings.

## Slide 50: Visual-Weld 7.5
  Updates – Home Page
Visual-Weld 7.5
Quick access to open new document, open file, open project & execute session
Quick access to recently opened files
Highlights of current version
One click access to latest news, services, support and contact
Acess to ESI Twitter, Face book and You tube
Survey Section for quick actions
One click Feedback section

## Slide 51: Visual-Weld 7.5
  Updates – Multi Db, *.DAT file reading.
Visual-Weld 7.5
Multi DB support for Material and for Functions
  User can assign materials to components by choosing the material from a wide range of material database files (*.mat). Visual-Weld generates a new .mat file with all materials selected from the db files. In a similar, you can assign functions by choosing them from a wide range of function database files (*.fct).
Supported loading of *.DAT files
  Any valid *.DAT file can be loaded directly into Visual-Weld. This facility allows you to load the DAT file which is generated in Sysweld or any other tool. You can modify the card data directly and export as a *.ASC file. This file can be used in Computation Manager. A log file is generated and posted as a hyper link on the console for your information.

## Slide 52: Visual-Weld 7.5
  Updates – Weld-HT Chaining
Visual-Weld 7.5
Weld-HT Chaining
  Heat Treatment project files are restarted if welding project files already exist in the current working directory. An option is given to select Weld - HT chaining or normal heat treatment export. Start time of the heat treatment project files is the end time of the last welding project file.
  * Due to limitation in handling material and function db chained data can’t be re-used to the full extent in this version.
Common windows between Pre and Post processors
  Pages and windows are now managed the same way across all applications for seamless navigation.

## Slide 53: Visual-Weld 7.5
  Updates – Work Flow Manager Updates
Visual-Weld 7.5
Block List for work flow managers for quick navigation

## Slide 54: Visual-Weld 7.5
  Updates – Explorer Updates
Visual-Weld 7.5
Enabled Page/File view tab and GLB tab in Welding application. GLB Tab allows user to quickly On or Off the desired entities globally.

## Slide 55: Visual-Weld 7.5
  Updates – Computation Manager Updates
Visual-Weld 7.5
Export for Cluster
  To allow you to export all the data files through the Computation Manager to solve large models on a cluster.

## Slide 56: Visual-Weld 7.5
  Updates – Other Updates
Visual-Weld 7.5
Proper material import from .MAT file for Heat Treatment is supported with HTD, HTL, HTQ and HTS tags.
Option to define “User Length Step” in the “Weld Pool’ section.
Free Air Cooling function is updated to use by default CONVECTIVE AND RADIATIVE LOSSES mm instead Heat Exchange With Air in the Function file.
Explorer is updated to retain the default *.ASC file infromation even on closing the Welding or HT advisor.
Not Yet Deposited Material by default "NO" in General Preferences.
Enhanced and Updated missed out tooltips in Welding and HT advisors.
Context Senstive help given for each steps in Welding and HT advisor.
Solver setting dialog is simplified.
Convert Element Type functionality is added in Tools menu.
Visual Weld generated vdb file can be loaded in any VE applications.
Visual Weld generated vdb compatability issue across platforms
Addressed many issues reported in previous versions.

## Slide 57: Outline
What is Visual-Weld?
Model Building
Welding Advisor
Weld Utilities
Heat Treatment Advisor
Post Processing & Report Generation
Tools & Customization
Discussions